## Slide 1: CS 480/680
Computer Graphics
Transformations
Dr. Frederick C Harris, Jr.

## Slide 2: Objectives
Introduce standard transformations
  Rotation
  Translation
  Scaling
  Shear
Derive homogeneous coordinate transformation matrices
Learn to build arbitrary transformation matrices from simple transformations

## Slide 3: General Transformations
A transformation maps points to other points and/or vectors to other vectors
Q=T(P)
v=T(u)

## Slide 4: Affine Transformations
Line preserving
Characteristic of many physically important transformations
  Rigid body transformations: rotation, translation
  Scaling, shear
Importance in graphics is that we need only transform endpoints of line segments and let implementation draw line segment between the transformed endpoints

## Slide 5: Pipeline Implementation
v
transformation
rasterizer
u
u
v
T
T(u)
T(v)
T(u)
T(u)
T(v)
T(v)
vertices
vertices
pixels
frame
buffer
(from application program)

## Slide 6: Notation
We will be working with both coordinate-free representations of transformations and representations within a particular frame
P,Q, R: points in an affine space
u, v, w: vectors in an affine space
a, b, g: scalars
p, q, r: representations of points
-array of 4 scalars in homogeneous coordinates
u, v, w: representations of points
-array of 4 scalars in homogeneous coordinates

## Slide 7: Translation
Move (translate, displace) a point to a new location
Displacement determined by a vector d
  Three degrees of freedom
  P’=P+d
P
P’
d

## Slide 8: How many ways?
Although we can move a point to a new location in infinite ways, when we move many points there is usually only one way
object
translation: every point displaced
by same vector

## Slide 9: Translation Using Representations
Using the homogeneous coordinate representation in some frame
p=[ x y z 1]T
p’=[x’ y’ z’ 1]T
d=[dx dy dz 0]T
Hence p’ = p + d or
x’=x+dx
y’=y+dy
z’=z+dz
note that this expression is in
four dimensions and expresses
point = vector + point

## Slide 10: Translation Matrix
We can also express translation using a
4 x 4 matrix T in homogeneous coordinates
p’=Tp where
T = T(dx, dy, dz) =
This form is better for implementation because all affine transformations can be expressed this way and multiple transformations can be concatenated together

## Slide 11: Rotation (2D)
Consider rotation about the origin by q degrees
  radius stays the same, angle increases by q
x’=x cos q –y sin q
y’ = x sin q + y cos q
x = r cos f
y = r sin f
x = r cos (f + q)
y = r sin (f + q)

## Slide 12: Rotation about the z axis
Rotation about z axis in three dimensions leaves all points with the same z
  Equivalent to rotation in two dimensions in planes of constant z
  or in homogeneous coordinates
  p’=Rz(q)p
x’=x cos q –y sin q
y’ = x sin q + y cos q
z’ =z

## Slide 13: Rotation Matrix
R = Rz(q) =

## Slide 14: Rotation about x and y axes
Same argument as for rotation about z axis
  For rotation about x axis, x is unchanged
  For rotation about y axis, y is unchanged
R = Rx(q) =
R = Ry(q) =

## Slide 15: Scaling
S = S(sx, sy, sz) =
x’=sxx
y’=syx
z’=szx
p’=Sp
Expand or contract along each axis (fixed point of origin)

## Slide 16: Reflection
corresponds to negative scale factors
original
sx = -1 sy = 1
sx = -1 sy = -1
sx = 1 sy = -1

## Slide 17: Inverses
Although we could compute inverse matrices by general formulas, we can use simple geometric observations
  Translation: T-1(dx, dy, dz) = T(-dx, -dy, -dz)
  Rotation: R -1(q) = R(-q)
    Holds for any rotation matrix
    Note that since cos(-q) = cos(q) and sin(-q)=-sin(q)
    R -1(q) = R T(q)
  Scaling: S-1(sx, sy, sz) = S(1/sx, 1/sy, 1/sz)

## Slide 18: Concatenation
We can form arbitrary affine transformation matrices by multiplying together rotation, translation, and scaling matrices
Because the same transformation is applied to many vertices, the cost of forming a matrix M=ABCD is not significant compared to the cost of computing Mp for many vertices p
The difficult part is how to form a desired transformation from the specifications in the application

## Slide 19: Order of Transformations
Note that matrix on the right is the first applied
Mathematically, the following are equivalent
p’ = ABCp = A(B(Cp))
Note many references use column matrices to represent points. In terms of column matrices
p’T = pTCTBTAT

## Slide 20: General Rotation About the Origin
q
x
z
y
v
A rotation by q about an arbitrary axis
can be decomposed into the concatenation
of rotations about the x, y, and z axes
R(q) = Rz(qz) Ry(qy) Rx(qx)
qx qy qz are called the Euler angles
Note that rotations do not commute
We can use rotations in another order but
with different angles

## Slide 21: Rotation About a Fixed Point other than the Origin
Move fixed point to origin
Rotate
Move fixed point back
M = T(pf) R(q) T(-pf)

## Slide 22: Instancing
In modeling, we often start with a simple object centered at the origin, oriented with the axis, and at a standard size
We apply an instance transformation to its vertices to
Scale
Orient
Locate

## Slide 23: Shear
Helpful to add one more basic transformation
Equivalent to pulling faces in opposite directions

## Slide 24: Shear Matrix
Consider simple shear along x axis
x’ = x + y cot q
y’ = y
z’ = z
H(q) =