## Slide 1: Modeling particle diffusion in laminar tube flow with spectral collocation
C. M. Thibeault, University of Nevada, Reno
F. C. Harris Jr., University of Nevada, Reno
and P. A. Tebbe Minnesota State University,
Mankato

## Slide 2: Overview
The spectral collocation method is a numerical approximation technique that seeks the solution of a differential equation using a finite series of infinitely differentiable basis functions.
This inherently global technique enjoys an exponential rate of convergence and has proven to be extremely effective in computational fluid dynamics.
Despite the initial complexity of understanding spectral collocation, the use of the method is relatively straight forward.
In our paper we present a complete example of applying this method to modeling particle diffusion in laminar tube flow.
  The included code, written for Octave, highlights the reduction of a partial differential equation into a matrix interpolation using spectral collocation.
The results are compared to an analytical solution for accuracy and a finite difference method for performance.

## Slide 3: Introduction: Laminar Flow
The fluid moves slowly in layers, without much mixing among the layers.

## Slide 4: Introduction: Spectral Collocation
The spectral method is a numerical modeling technique for approximating the solution of partial and ordinary differential equations.
  Related to the method of weighted residuals, spectral methods employ infinitely differentiable functions as trial functions.
  The result is a global method with an exponential rate of convergence for problems with smooth solutions.
  Since the discovery of fast Fourier transforms the use and practicality of spectral methods has steadily increased.
  There has been broad success in several areas including Weather, Turbulence, Seismic, and Quantum Modeling

## Slide 5: Introduction: Spectral Collocation
There are several features that set spectral collocation methods apart from other numerical solutions to partial differential equations.
  The first is the computational domain.
    In Finite Element (FE) modeling for example, the overall physical domain is broken up into a number of sub-domains (elements) and a local basis function is chosen to be nonzero over a small number of sub-intervals within that domain.
    Conversely, spectral methods chose a basis function that is global to the entire computational domain and is nonzero except at isolated points.
    It is this reason that spectral methods are often referred to as a global numerical method.

## Slide 6: Introduction: Spectral Collocation
  The second distinguishing feature of spectral methods is the choice of basis functions.
    Spectral methods select basis functions that are high degree polynomials or trigonometric polynomials that are infinitely differentiable.
    The basis functions for FE methods are generally low-order polynomials and as stated before, local in nature.
    Because of this, FE methods are better suited for complex geometries but suffer from lower accuracy as compared to spectral methods.

## Slide 7: Introduction: Particle diffusion in laminar tube flow
When aerosol particulates are exposed to a concentration gradient they diffuse from high to low concentrations by Brownian motion.
Similarly, when those particles are dispersed in a fluid that is traveling down a tube or between parallel plates, the walls of the vessel will act like a sink to those particles—by the same Brownian motion.
For most models of this process the concentration at the wall is taken to be zero and the particles will not only diffuse radially to the wall but will also deposit there.
This diffusion process is important in a number of applications
  Desired—such as air cleaning, hot-gas filtration, optical fiber manufacturing, and thin film production
  Undesired—pipe fouling, micro-contamination and corrosion

## Slide 8: Introduction: Particle diffusion in laminar tube flow
The modeling of aerosol deposition in a tube is a well characterized problem and there have been several analytical solutions for the deposition efficiency.
  The first was developed by Gormley and Kennedy in 1949.
    This is the benchmark solution referred to by most of the subsequent studies.
These analytical treatments make this problem ideal for demonstrating the accuracy of numerical methods and the application of spectral collocation to this problem is unique to this paper.

## Slide 9: Introduction: Navier-Stokes equations
The motion of fluid in space is described by the Navier- Stokes equations.
Emerging from Newton’s second law, the Navier-Stokes equations relate the gradients of the dependent variables to form a system of nonlinear partial differential equations.
  Conservation of Momentum
  Conservation of Energy
  Conservation of Mass

## Slide 10: Introduction: Navier-Stokes equations
For the simple diffusion problem it is assumed that there is no formulation of aerosols and the mass transfer along the direction of flow due to diffusion can be neglected.
These are both valid as long as the Peclet number is significantly greater than 1
  meaning the movement due to advection is significantly higher than the movement due to diffusion.
  We therefore end up with:

## Slide 11: Introduction: Analytical Solution
The analytical solution for this was first developed by Gormley and Kennedy and slightly reformed by Hinds.
This was found to closely approximate experimental results and is used here as a way to estimate the accuracy of the spectral method.
The solution is defined as:
  Where m is the
  dimensionless coefficient

## Slide 12: Numerical Methods
To generalize, the spectral collocation, or pseudospectral, method interpolates all of the discrete data and then approximates the derivative of the interpolant along that data globally.
In this case, the global space is a discrete grid of Gauss-Lobatto-Chebyshev points and interpolants are Chebyshev polynomials.
The domain of the points lie along the domain [−1, 1] where Chebyshev polynomials remain analytic and convergence of the spectral series can be ensured.

## Slide 13: Numerical Methods
Spectral collocation is based on differentiation matrices
The differentiation matrix, DN, approximates the derivative of a vector with points at the Chebyshev extreme points.
Higher-order derivatives can be found by raising the first-order differentiation matrix by an exponent corresponding to the order (i.e. squaring the matrix for the second derivative).
Finally, two-dimensional differentiation matrices can be constructed by taking the Kronecker product of two one-dimensional differentiation matrices

## Slide 14: Chebyshev Differentiation matrix
This figure illustrates how these points are constructed.
The (N −1)×(N −1) matrix is indexed by j for columns and i for rows.

## Slide 15: Octave code for generating a spectral differentiation matrix
Constructing this matrix can be condensed using vectorized functions available inMATLAB and Octave,
However, expanding this formulation better illustrates the matrix construction and improves performance.

## Slide 16: Code Development
Once the differentiation matrices are generated —Listing 1— their application follows from basic linear algebra.
The solution for this problem, including initialization, boundary condition enforcement, solving, and post-condition, is presented in Listing 2
  notice that the bulk of this code is taken up by comments.
  The use of built-in MATLAB/Octave functions eases the programming burden
  however, converting this code to a more efficient language would be reasonable.
  More importantly, would be generalizing this technique into a library for solving generic partial differential equations.

## Slide 17: Solving for particle deposition using spectral collocation

## Slide 18: Results
The output from Listing 2 is presented next for different diffusion coefficients.
The affect the diffusion coefficient has is clear from these plots.
For this a grid of 41x41 was used and plotted directly.
However, a cubic spline interpolation can be used to further improve the estimation and create smoother solutions.
  This is also one strategy for improving the interpretation of results from smaller grid sizes.

## Slide 19: Particle diffusion along an identical tube for different diffusion coefficients
There are a number of parameters that affect the efficiency of the particle deposition.
  In this case as the diffusion coefficient is increased for an identical pipe, a larger number of particles will deposit on the pipe walls.
  For this a square grid of size 41x41 was used.

## Slide 20: Accuracy of spectral method compared to analytical solution
As the grid size is increased the accuracy of the spectral method increases as compared to the analytical solution.
The left hand axis is the penetration as calculated by Equation 16 as the dimensionless diffusion coefficient μ is changed.
The right hand axis is the difference between the two methods at each data point (blue line).

## Slide 21: Spectral collocation compared to a naive finite difference method
Speedup between the methods (top). As the grid size is changed equally for both methods the speedup for the spectral method decreases.
Accuracy compared to the analytical solution (bottom). Initially the finite difference method (blue line) is slightly more accurate.
  However, as the grid size is increased the spectral method’s (black line) accuracy continues to improve—whereas the finite difference method does not improve at as fast a rate.

## Slide 22: Conclusion
When applied to a classic fluid dynamics problems the spectral collocation method is in excellent agreement with previously published results.
Its computational efficiency coupled with its high accuracy make it ideally suited to this class of problems.
Although this is a well classified example, this work contributes a method for approximating their solutions that is more accurate and computationally tractable.

## Slide 23: Future Work
Despite only presenting a specific example, this paper lays the foundation for extending this work to a generic partial differential equation library.
In addition, migrating to a more efficient programming language is also something that will be done in the future.
Finally, although a steady-state problem was presented here, the transition into solving a dynamic version of this equation would simply involve using spectral collocation in space and a discrete (i.e. a leap frog method) in time

## Slide 24: Modeling particle diffusion in laminar tube flow with spectral collocation
C. M. Thibeault, University of Nevada, Reno
F. C. Harris Jr., University of Nevada, Reno
and P. A. Tebbe Minnesota State University,
Mankato