## Slide 1: VGX Hardware Implementation
Scott Fritzinger
University of Nevada, Reno

## Slide 2: Box Mock-up
Lightweight PVC pipe
High-density pressed board
Easily reconfigurable
  Mount extra cameras
  Cut holes
  Add extra supports
Inexpensive
  Several can be made for low-cost
Blue/green screen backdrop
  Background removal

## Slide 3: I/O Bus Decision
Required Throughput
  8 cameras, 30fps
    9.22 MB/s of grayscale data
    27.6 MB/s of RGB data
On-board bus considerations
  PCI Bus: 133 – 266 MB/s
Camera bus considerations
  USB: 1.5 MB/s
  USB 2.0: 60 MB/s
  FireWire (IEEE1394): 50 MB/s
FireWire – Off-the-shelf components

## Slide 4: Cameras
PT Grey DragonFly
  Self-synchronizing (required for reconstruction)
  640x480 30fps
  Raw Bayer data
    Color for no cost in bandwidth
    Overhead added in image processing
  Several Mounting Options
    C-bracket and full box enclosure
  Various Lens Options
    C-Mount lens option for off-the-shelf lens
DragonFly Camera
(Dimensions: 2” x 2“ )
Sample Bayer Pattern

## Slide 5: Capture Software
Linux 2.4.20
  FireWire Support
  Custom configuration for higher performance
Custom-made capture software for high-throughput
DMA for fast transfers
Journaled file-system
  Fast reads/writes
Output buffering
  Fewer disc writes with larger data blocks

## Slide 6: Video File Playback
Video files
  Raw Bayer data
  Standard PGM header with comments for format extension
  Allows quick preview in any PGM compliant image viewer
QT 3.1 Interface
  Rapid development
  Cross-Platform (Linux, Windows, Mac)

## Slide 7: Questions?
VGX Hardware Implementation