## Slide 1: Autonomous Mobile Robots CPE 470/670
Lecture 8
Instructor: Monica Nicolescu

## Slide 2: Control Architectures
Feedback control is very good for doing one thing
  Wall following, obstacle avoidance
Most non-trivial tasks require that robots do multiple things at the same time
How can we put multiple feedback controllers together?
Find guiding principles for robot programming

## Slide 3: Control Architecture
A robot control architecture provides the guiding principles for organizing a robot’s control system
It allows the designer to produce the desired overall behavior
The term architecture is used similarly as “computer architecture”
  Set of principles for designing computers from a collection of well-understood building blocks
The building-blocks in robotics are dependent on the underlying control architecture

## Slide 4: Software/Hardware Control
Robot control involves hardware, signal processing and computation
Controllers may be implemented:
  In hardware: programmable logic arrays
  In software: conventional program running on a processor
The more complex the controller, the more likely it will be implemented in software
In general, robot control refers to software control

## Slide 5: Languages for Robot Programming
Control architectures may be implemented in various programming languages
Turing universality: a programming language is Turing universal if it has the following capabilities:
  Sequencing: a then b then c
  Conditional branching: if a then b else c
  Iteration: for a = 1 to 10 do something
With these one can compute the entire class of computable functions
All major programming languages are Turing Universal

## Slide 6: Computability
Architectures are all equivalent in computational expressiveness
  If an architecture is implemented in a Turing Universal programming language, it is fully expressive
  No architecture can compute more than another
The level of abstraction may be different
Architectures, like languages are better suited to a particular domain

## Slide 7: Organizing Principles
Architectures are built from components, specific for the particular architecture
The ways in which these building blocks are connected facilitate certain types of robotic design
Architectures do greatly affect and constrain the structure of the robot controller (e.g., behavior representation, granularity, time scale…)
Control architectures do not constrain expressiveness
  Any language can compute any computable function  the architecture on top of it cannot further limit it

## Slide 8: Uses of Programming Languages
Programming languages are designed for specific uses
  Web programming
  Games
  Robots
A control architecture may be implemented in any programming language
Some languages are better suited then others
  Standard: Lisp, C, C++
  Specialized: Behavior-Language, Subsumption Language

## Slide 9: Specialized Languages for Robot Control
Why not use always a language that is readily available (C, Java)?
Specialized languages facilitate the implementation of the guiding principles of a control architecture
  Coordination between modules
  Communication between modules
  Prioritization
  Etc.

## Slide 10: Robot Control Architectures
There are infinitely many ways to program a robot, but there are only few types of robot control:
  Deliberative control (no longer in use)
  Reactive control
  Hybrid control
  Behavior-based control
Numerous “architectures” are developed, specifically designed for a particular control problem
However, they all fit into one of the categories above

## Slide 11: Comparing Architectures
The previous criteria help us to compare and evaluate different architectures relative to specific robot designs, tasks, and environments
Architectures can be classified by the way in which they treat:
  Time-scale (looking ahead)
  Modularity
  Representation
There is no perfect recipe for finding the right control architecture

## Slide 12: Time-Scale and Looking Ahead
How fast does the system react? Does it look into the future?
Deliberative control
  Look into the future (plan) then execute  long time scale
Reactive control
  Do not look ahead, simply react  short time scale
Hybrid control
  Look ahead (deliberative layer) but also react quickly (reactive layer)
Behavior-based:
  Look ahead while acting

## Slide 13: Modularity
Refers to the way the control system is broken into components
Deliberative control
  Sensing (perception), planning and acting
Reactive control
  Multiple modules running in parallel
Hybrid control
  Deliberative, reactive, middle layer
Behavior-based:
  Multiple modules running in parallel

## Slide 14: Representation
Representation is the form in which the control system internally stores information
  Internal state
  Internal representations
  Internal models
  History
What is represented and how it is represented has a major impact on robot control
State refers to the "status" of the system itself, whereas "representation" refers to arbitrary information that the robot stores

## Slide 15: An Example
Consider a robot that moves in a maze: what does the robot need to know to navigate and get out?
Store the path taken to the end of the maze
  Straight 1m, left 90 degrees, straight 2m, right 45 degrees
  Odometric path
Store a sequence of moves it has made at particular landmark in the environment
  Left at first junction, right at the second, left at the third
  Landmark-based path

## Slide 16: Topological Map
Store what to do at each landmark in the maze
  Landmark-based map
The map can be stored (represented) in different forms
  Store all possible paths and use the shortest one
  Topological map: describes the connections among the landmarks
  Metric map: global map of the maze with exact lengths of corridors and distances between walls, free and blocked paths: very general!
The robot can use this map to find new paths through the maze
Such a map is a world model, a representation of the environment

## Slide 17: World Models
Numerous aspects of the world can be represented
  self/ego: stored proprioception, self-limits, goals, intentions, plans
  space: metric or topological (maps, navigable spaces, structures)
  objects, people, other robots: detectable things in the world
  actions: outcomes of specific actions in the environment
  tasks: what needs to be done, in what order, by when
Ways of representation
  Abstractions of a robot’s state & other information

## Slide 18: Model Complexity
Some models are very elaborate
  They take a long time to construct
  These are kept around for a long time throughout the lifetime of the robot
  E.g.: a detailed metric map
Other models are simple
  Can be quickly constructed
  In general they are transient and can be discarded after use
  E.g.: information related to the immediate goals of the robot (avoiding an obstacle, opening of a door, etc.)

## Slide 19: Models and Computation
Using models require significant amount of computation
Construction: the more complex the model, the more computation is needed to construct the model
Maintenance: models need to be updated and kept up-to-date, or they become useless
Use of representations: complexity directly affects the type and amount of computation required for using the model
Different architectures have different ways of handling representations

## Slide 20: An Example
Consider a metric map
Construction:
  Requires exploring and measuring the environment and intense computation
Maintenance:
  Continuously update the map if doors are open or closed
Using the map:
  Finding a path to a goal involves planning: find free/navigational spaces, search through those to find the shortest, or easiest path

## Slide 21: Simultaneous Mapping and Localization

## Slide 22: Cooperative Mapping and Localization

## Slide 23: Reactive Control
Reactive control is based on tight (feedback) loops connecting a robot's sensors with its effectors
Purely reactive systems do not use any internal representations of the environment, and do not look ahead
  They work on a short time-scale and react to the current sensory information
Reactive systems use minimal, if any, state information

## Slide 24: Collections of Rules
Reactive systems consist of collections of reactive rules that map specific situations to specific actions
Analog to stimulus-response, reflexes
  Bypassing the “brain” allows reflexes to be very fast
Rules are running concurrently and in parallel
Situations
  Are extracted directly from sensory input
Actions
  Are the responses of the system (behaviors)

## Slide 25: Complete Control Space
The entire state space of the robot consists of all possible combinations of the internal and external states
A complete mapping from these states to actions is needed such that the robot can respond to all possibilities
This is would be a tedious job and would result in a very large look-up table that takes a long time to search
Reactive systems use parallel concurrent reactive rules  parallel architecture, multi-tasking

## Slide 26: Incomplete Mappings
In general, complete mappings are not used in hand-designed reactive systems
The most important situations trigger the appropriate reactions
Default responses are used to cover all other cases
E.g.: a reactive safe-navigation controller
  If left whisker bent then turn right
  If right whisker bent then turn left
  If both whiskers bent then back up and turn left
  Otherwise, keep going

## Slide 27: Example – Safe Navigation
A robot with 12 sonar sensors, all around the robot
Divide the sonar range into two zones
  Danger zone: things too close
  Safe zone: reasonable distance to objects
if minimum sonars 1, 2, 3, 12 < danger-zone and not-stopped
then stop
if minimum sonars 1, 2, 3, 12 < danger-zone and stopped
then move backward
otherwise
move forward
This controller does not look at the side sonars
1
2
3
4
5
6
7
8
9
10
11
12

## Slide 28: Example – Safe Navigation
For dynamic environments, add another layer
if sonar 11 or 12 < safe-zone and
sonar 1 or 2 < safe-zone
then turn right
if sonar 3 or 4 < safe-zone
then turn left
The robot turns away from the obstacles before getting too close
The combinations of the two controllers above  collision-free wandering behavior
Above we had mutually-exclusive conditions
1
2
3
4
5
6
7
8
9
10
11
12

## Slide 29: Mutually Exclusive Situations
If the set of situations is mutually exclusive:
 only one situation can be met at a given time
 only one action can be activated
Often is difficult to split up the situations this way
To have mutually exclusive situations the controller must encode rules for all possible sensory combinations, from all sensors
This space grows exponentially with the number of sensors

## Slide 30: Action Selection
In most cases the rules are not triggered by unique mutually-exclusive conditions
  More than one rule can be triggered at the same time
  Two or more different commands are sent to the actuators!!
Deciding which action to take is called action selection
Arbitration: decide among multiple actions or behaviors
Fusion: combine multiple actions to produce a single command

## Slide 31: Arbitration
There are many different types of arbitration
Arbitration can be done based on:
a fixed priority hierarchy
  rules have pre-assigned priorities
a dynamic hierarchy
  rules priorities change at run-time
learning
  rule priorities may be initialized and are learned at run-time, once or continuously

## Slide 32: Multi-Tasking
Arbitration decides which one action to execute
To respond to any rule that might become triggered all rules have to be monitored in parallel, and concurrently
  If no obstacle in front  move forward
  If obstacle in front  stop and turn away
  Wait for 30 seconds, then turn in a random direction
Monitoring rules in sequence may lead to missing important events, or failing to react in real time
Reactive systems must support parallelism
  The underlying programming language must have multi-tasking abilities

## Slide 33: Designing Reactive Systems
How to can we put together multiple (large number) of rules to produce effective, reliable and goal directed behavior?
How do we organize a reactive controller in a principled way?
The best known reactive architecture is the Subsumption Architecture (Rod Brooks, MIT, 1985)

## Slide 34: Vertical v. Horizontal Systems
Traditional (SPA):
sense – plan – act
Subsumption:

## Slide 35: Biological Inspiration
The inspiration behind the Subsumption Architecture is the evolutionary process:
  New competencies are introduced based on existing ones
Complete creatures are not thrown out and new ones created from scratch
  Instead, solid, useful substrates are used to build up to more complex capabilities

## Slide 36: The Subsumption Architecture
Principles of design
  systems are built from
  the bottom up
  components are task-achieving
  actions/behaviors (avoid-obstacles, find-doors, visit-rooms)
  components are organized in layers, from the bottom up
  lowest layers handle most basic tasks
  all rules can be executed in parallel, not in a sequence
  newly added components and layers exploit the existing ones

## Slide 37: Subsumption Layers
First, we design, implement and debug layer 0
Next, we design layer 1
  When layer 1 is designed, layer 0 is taken into consideration and utilized, its existence is subsumed
  Layer 0 continues to function
Continue designing layers, until the desired task is achieved
Higher levels can
  Inhibit outputs of lower levels
  Suppress inputs of lower levels
level 2
level 1
level 0
sensors
actuators
AFSM
inputs
outputs
suppressor
inhibitor
I
s

## Slide 38: Subsumption Language and AFSMs
The original Subsumption Architecture was implemented using the Subsumption Language
It was based on finite state machines (FSMs) augmented with a very small amount of state (AFSMs)
AFSMs were implemented in Lisp
AFSM
inputs
outputs
suppressor
inhibitor
I
s

## Slide 39: Subsumption Language and AFSMs
Each behavior is represented as an augmented finite state machine (AFSMs)
Stimulus (input) or response
(output) can be inhibited or
suppressed by other active behaviors
An AFSM can be in one state at a time, can receive one or more inputs, and send one or more outputs
AFSMs are connected with communication wires, which pass input and output messages between them; only the last message is kept
AFSMs run asynchronously
AFSM
inputs
outputs
suppressor
inhibitor
I
s
collide
halt
sonar

## Slide 40: Networks of AFSMs
Layers represent task achieving behaviors
  Wandering, avoidance, goal seeking
Layers work concurrently and asynchronously
A Subsumption Architecture controller,
using the AFSM-based programming
language, is a network of AFSMs divided into layers
Convenient for incremental system design
level 2
level 1
level 0

## Slide 41: Wandering in Subsumption
Brooks ‘87

## Slide 42: Readings
M. Matarić: Chapter 11, 12, 14